## Slide 1: Desperately Seeking Default
Geoff Huston
APNIC

## Slide 2: In the Telephone Network
All telephones were equally reachable
Anyone could dial anyone else

## Slide 3: In the Telephone Network
Are all connected endpoints equally reachable?
Can anyone can reach anyone else?
Internet

## Slide 4: In the Telephone Network
Are all connected endpoints are equally reachable?
Can anyone can reach anyone else?
Internet
No!

## Slide 5: In the Telephone Network
Are all connected endpoints are equally reachable?
Can anyone can reach anyone else?
Internet
NATs and Firewall Filters changed our conception of the Internet from a peer-to-peer network to a limited client/server architecture.
Our current expectations are that if you stand up a public service on port 80 (or 443 for that matter) outside of a NAT, then maybe everyone can reach you, but otherwise, no.
No!

## Slide 6: In the Telephone Network
All connected endpoints are equally reachable
Can anyone can reach anyone else?
Internet

## Slide 7: In the Telephone Network
All connected endpoints are equally reachable
Can anyone can reach anyone else?
Internet
We might THINK this, but is it true ALL the time?

## Slide 8: What do we see?
On the Internet is everyone really connected to everyone else?

## Slide 9: How We See
We use an online ad to present a sequence of small fetches to the user’s browser

## Slide 10: How We See
The sequence of tests is used to test a number of types of actions including fetches of IPv4,
IPv6 and Dual stack

## Slide 11: How We See
We use tcpdump to record all packet activity at the experiment’s servers

## Slide 12: What we see: Connection Failure
Outbound SYN
Busted SYN ACK
Return path
What the server sees is an incoming SYN, but no matching incoming ACK
server
client

## Slide 13: Daily IPv6 Failures
6to4 failure: around 10%
Average IPv6 failure: around 2%
Unicast IPv6 failure: around 1.5%

## Slide 14: Daily IPv6 Unicast Address Failures
1.5% failure rate

## Slide 15: IPv6 Failures
1.5% failure for unicast V6 is unacceptable!
Why is this happening
  Auto-tunnelling?
  Lousy CPE firmware?
  Strange firewall filters?
But is all of this due to local configuration / equipment?
What is the comparable view in IPv4?

## Slide 16: IPv4 Connection Failure
0.2% failure rate

## Slide 17: IPv4 Failures
IPv4 failures are around 1 in 500
And we are pretty sure its NOT:
  Auto-tunnelling
  Lousy CPE firmware
  Strange firewall filters
So what is the reason for this residual asymmetric failure rate?
Is it asymmetric routing connectivity?

## Slide 18: Route Views Routing Table

## Slide 19
25 Years of Routing the Internet
This is a compound view pulled together from each of the IPv4 routing peers of Route Views and RIS

## Slide 20: IPv4 - 2015/16 IPv4 Route Views + RIS
This is a view pulled together from each of the routing peers of Route Views and RIS
That’s a range of 100,000 routes!

## Slide 21: Different peers see a slightly different Internet
But is this just traffic engineering more specifics?
Or do different peers see a different set of reachable addresses in the routing table?

## Slide 22: Address Span (Route Views + RIS data sets)

## Slide 23: Address Span (Route Views + RIS data sets)
15 M Addresses

## Slide 24: What does this mean?
Each peer of RouteViews and RIS announces a span of addresses that appears to be a unique span.
In total, these spans agree with other to within ~20M addresses, but this means that there are potentially some 20M uniquely addressed endpoints that cannot be reached from all other endpoints.
This variation is stable over time for each peer, so its not transient routing that is generating this – the reasons for this difference in reachability are structural

## Slide 25: What about IPv6?

## Slide 26: The Route Views view of IPv6
World IPv6 Day
IANA IPv4 Exhaustion

## Slide 27: Number of IPv6 Routes in 2015/16
That’s a
range of 2,300
routes!

## Slide 28: IPv6 Announced Address Span Variation (RV + RIS)

## Slide 29: IPv6 Announced Address Span Variation (RV + RIS)

## Slide 30: What is “default”?
We don’t know!
There is no “default” route set that we can all agree on

## Slide 31: What is “default”?
At best “default” is an informal quorum
  So lets define this quorum by arbitrarily setting the quorum threshold at 2/3
  i.e. if 2/3 of the peers of a route collector advertise a route then it is part of the default quorum.
Individual peer networks will contain route sets that differ from this quorum by having both additional prefixes and holes.
  Lets look at the variance from the quorum

## Slide 32: A “Quorum” deviation view of IPv4

## Slide 33: A magnified view

## Slide 34: IPv6 “Quorum” Deviation

## Slide 35: Zooming In

## Slide 36: And Again

## Slide 37: Quorum Deviation for RVA IPv4 Peers (18th August 2016)

## Slide 38: Quorum Deviation for RIS IPv4 Peers

## Slide 39: Quorum Deviation: IPv6, RVA

## Slide 40: Quorum Deviation: IPv6, RIS

## Slide 41: It’s structural, not temporal
There is a visible stability to this deviation from the quorum route set
  The variation from the quorum is long–term stable, and does not rapidly self-correct – its not a transient routing state
We appear to assume that all Tier 1 providers, and their Tier 2, 3, … resellers offer the same reachability set as each other – i.e. ”default” is consistent everywhere
But this is not necessarily the case all the time for every address in the routing system
“Default” appears to vary by provider and by location
  E.g.: 25 April, 1600 UTC:
    AS2914: RouteViews 2,808,560,896 addresses
    RIS: 2,807,358,208

## Slide 42: ”Default” is a market outcome
There is no ”global route arbiter”
There is no way to enrol a route into a global Internet default route set
There is no single common definition of “default”
Instead ”default” is a market outcome
  You buy default from a transit
    You hope your transit is offering you what it promised – but you just can’t tell
  You add your route to default via a transit
    You hope that this will propagate reachability tp your network to all parts of the Internet – but you just can’t tell

## Slide 43: So What?
Surely all this is patched up by the widespread use of a routing default entry in addition to specific routes? (*)
* Internet Optometry: Assessing the Broken Glasses in Internet Reachability”,
R. Bush, O. Maennel, M. Roughan, S Uhlig, ACM SIGCOMM IMC, 2009

## Slide 44: So What?
Surely all this is patched up by the widespread use of a routing default entry in addition to specific routes?
  Well, not really
  Default points along upstream transits
  It does not patch downstreams
A
B
Route to B not propagated on this connection
Packet from B to A follows explicit route
Packet from B to A follows default and then
dropped

## Slide 45: To Recap: What is causing this?

## Slide 46: To Recap: What is causing this?
Could part of this be due to connectivity failure?

## Slide 47: Can we confirm this?
Outbound SYN
server
client

## Slide 48: Can we confirm this?
Outbound SYN
SYN ACK
Return path
server
client

## Slide 49: Can we confirm this?
Outbound SYN
Busted SYN ACK
Return path
server
client
router

## Slide 50: Can we confirm this?
Outbound SYN
Busted SYN ACK
Return path
server
client
router
ICMP Dest Unreachable

## Slide 51: Can we confirm this?
Outbound SYN
Busted SYN ACK
Return path
server
client
router
ICMP Dest Unreachable
What the server sees is an incoming SYN, and then an ICMP destination unreachable

## Slide 52: And we do see this … here’s an example
14:16:05.999497 IP (tos 0x0, ttl 55, id 31005, offset 0, flags [none], proto ICMP (1), length 80)
84.41.108.74 > 139.162.146.97: ICMP host 46.163.63.47 unreachable, length 60
Outer packet is an ICMP Packet with a “destination unreachable” code sent to the server from the router at address 84.41.108.74

## Slide 53: And we do see this … here’s an example
14:16:05.999497 IP (tos 0x0, ttl 55, id 31005, offset 0, flags [none], proto ICMP (1), length 80)
84.41.108.74 > 139.162.146.97: ICMP host 46.163.63.47 unreachable, length 60
Outer packet is an ICMP Packet with a “destination unreachable” code sent to the server from the router at address 84.41.108.74
IP (tos 0x0, ttl 57, id 0, offset 0, flags [DF], proto TCP (6), length 52)
139.162.146.97.443 > 46.163.63.xx.52087: Flags [S.], cksum 0x5130 (correct), seq 3917125220, ack 685287936, win 29200, options [mss 1460,nop,nop,sackOK,nop,wscale 7], length 0
Payload packet is a SYN+ACK packet

## Slide 54: In the Telephone Network
All connected endpoints are equally reachable
Anyone can reach anyone else
Internet
Almost
almost
most of the time!

## Slide 55: In the Telephone Network
All connected endpoints are equally reachable
Anyone can reach anyone else
Internet
Almost
almost
most of the time!
As long as all the feeder access networks can connect to Facebook, Google, Netflix, Ebay, Amazon,… then nobody seems to care enough any more to be motivated to fix this
What we now have in 2016 is a tier 1 CDN feeder system. The internet is no longer a true uniquitous fully connected peer network, and our collective care factor about that is pretty low~
And that makes me sad!

## Slide 56: Thanks!